## Slide 1: Nepal Flood & Weather: Next-Day River Discharge Prediction

## Slide 2: Dataset at a glance
Coverage
Daily records, 1 Jan 2023 to 31 Aug 2026. 13,390 rows x 19 columns.
Stations
10 gauges, incl. Kusum, Belsot, Chameliya/Nayalbadi, Devghat, Khokana.
Variables
10 weather fields, 8 date/station fields, 1 target: river_discharge_m3s.
Quality
0 missing values, 0 duplicate rows, 0 duplicate date-station pairs.

## Slide 3: Station discharge varies 180x
Chart: 
| Kusum | Belsot | Chameliya/Nayalbadi | Bahrabise | Devghat | Khokana | Chatara | Rasuwagadhi | Chisapani | Bhada Bridge
Mean discharge | 125.81 | 33.03 | 31.39 | 5.05 | 2.33 | 1.66 | 1.49 | 1.41 | 0.85 | 0.7
Mean discharge in m³/s
Kusum averages 125.8, Bhada Bridge 0.7
One scale for all stations hides small rivers
Motivates station one-hot encoding and station-specific flood thresholds

## Slide 4: A heavily skewed target
1.88
median m³/s
20.37
mean m³/s
84.33
std deviation
3,176
max m³/s
Chart: IQR outlier counts
| rain_mm | precipitation_mm | river_discharge | wind_gusts | wind_speed | precip_hours
IQR outliers | 1915 | 1860 | 1379 | 832 | 522 | 345
Extremes were kept: they are the flood signal. Log transform used for the histogram.

## Slide 5: The monsoon dominates the year
Chart: m³/s
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Mean discharge | 4.31 | 3.8 | 3.53 | 3.2 | 3.25 | 6.31 | 53.72 | 72.46 | 52.97 | 28.61 | 8.74 | 5.05
Peak: August, 72.46 m³/s
Surge begins in June (6.3), jumps in July (53.7)
Dry months sit near 3-4 m³/s
Month is a strong predictor

## Slide 6: When do unusually high flows occur?
Chart: 
| Jun | Jul | Aug | Sep | Oct | Nov
Days above p95 | 7 | 174 | 346 | 88 | 49 | 2
666 station-days exceed their own 95th percentile
Aug alone holds 346; none in Jan-May or Dec
All 10 largest discharges belong to Kusum
Record: 3,175.87 m³/s on 28 Sep 2024 with only 8.4 mm rain: flood driven by upstream and antecedent water

## Slide 7: Weather vs discharge: weak links
Chart: 
| dew_point | temperature | humidity | soil_moisture | precip_hours | rain_mm | precipitation | wind_speed | wind_gusts | wind_dir
Correlation | 0.226 | 0.178 | 0.172 | 0.152 | 0.145 | 0.1 | 0.099 | 0.052 | -0.009 | -0.041
Pooled |r| never exceeds 0.23
Dew point leads; same-day rain only 0.10
Why: stations differ 100x in scale, and rain reaches the gauge with a delay
Fix: lag and rolling rainfall, per-station view

## Slide 8: Stations compared on a log scale
Kusum, Chameliya and Belsot have the highest medians
Spreads span 3+ orders of magnitude
Long upper whiskers = flood spikes
Station identity is essential model information

## Slide 9: Feature engineering pipeline
Rain lags
Previous 1, 2 and 3 day rainfall
Rolling rain
3-day and 7-day sums, 7-day mean (shifted 1 day)
Discharge history
Lag 1, lag 2, 7-day mean
Calendar + station
Year, month, 10 one-hot stations
All lags computed per station after sorting by date, so no cross-station leakage
35 features = 14 raw + 11 engineered + 10 station dummies
70 warm-up rows dropped (13,390 to 13,320); 10 more lost to the next-day target (13,310)

## Slide 10: Time-based train/test split
TRAIN 10,630 rows
TEST 2,680
9 Jan 2023
7 Dec 2025 (cutoff)
31 Aug 2026
Cutoff at the 80th percentile of dates; split on target_date, with assertions confirming no overlap
Thresholds and scaler fitted on training data only
Test window covers the full 2026 monsoon, a stringent out-of-time check
Caveat: test contains one monsoon season

## Slide 11: Regression model comparison
Model | MAE | RMSE | R²
Linear Reg. | 6.06 | 15.04 | 0.934
Random Forest | 2.42 | 16.66 | 0.920
Grad. Boosting | 2.84 | 19.34 | 0.892
Decision Tree | 3.11 | 23.08 | 0.846
Chart: 
| LR | RF | GB | DT
MAE | 6.06 | 2.42 | 2.84 | 3.11
RMSE | 15.04 | 16.66 | 19.34 | 23.08
Metrics in m³/s. RF wins MAE; Linear Regression wins RMSE and R².

## Slide 12: Linear vs Random Forest
Linear Regression
Best RMSE (15.04) and R² (0.934), driven by large peaks.
But MAE is 6.06, and it predicts negative discharge on low flows (-1.16 vs actual 1.64), which is physically impossible.
Random Forest (preferred)
Lowest MAE (2.42): accurate on the many low-flow days (1.78 vs 1.77 actual).
Larger misses at peak surges raise RMSE to 16.66.
No negative outputs; captures non-linear behaviour.

## Slide 13: Random Forest: actual vs predicted
Points hug the diagonal, with scatter at high flows. Kusum time series (right) follows the 2026 monsoon surge closely.

## Slide 14: Error analysis: largest flows
Date | Actual | Predicted | Error
19 Jul 2026 | 742.0 | 782.2 | -40.2
29 Aug 2026 | 655.2 | 520.0 | +135.1
18 Jul 2026 | 637.3 | 335.6 | +301.7
24 Aug 2026 | 635.8 | 667.9 | -32.1
30 Aug 2026 | 621.3 | 674.0 | -52.7
All top-10 flows are Kusum
Biggest miss: 18 Jul, a surge onset under-predicted by 302 m³/s
Hardest station: Kusum
Easiest: low-flow gauges (Bhada Bridge, Chisapani); per-station error not in notebook
Values in m³/s; error = actual - predicted.

## Slide 15: What drives next-day discharge
Chart: 
| discharge (today) | temperature | rain_mm | precipitation | discharge 7d mean | dew point | precip hours | rain lag 1 | soil moisture | discharge lag 1
Importance | 0.8136 | 0.0367 | 0.0233 | 0.021 | 0.0192 | 0.0169 | 0.012 | 0.0116 | 0.0104 | 0.0049
Current discharge alone = 81.4%
River flow is highly persistent
Weather and rainfall refine, not drive, the forecast
Persistence baseline needed to prove added skill

## Slide 16: Did feature engineering help?
Chart: 
| MAE | RMSE
Baseline | 2.4708 | 17.8201
Engineered | 2.4167 | 16.6552
-2.19%
MAE
-6.54%
RMSE
R² rose from 0.908 to 0.920
Gain is modest because raw discharge already carries most of the signal
Biggest benefit: fewer large errors (RMSE)

## Slide 17: High-flow classification setup
Station | p90 m³/s | Station | p90 m³/s
Kusum | 427.75 | Chatara | 4.57
Belsot | 94.68 | Rasuwagadhi | 3.59
Chameliya | 92.29 | Chisapani | 2.63
Bahrabise | 13.68 | Bhada Bridge | 2.66
Devghat | 6.29 | Khokana | 5.00
Label 1 if next-day flow exceeds the station's train-set 90th percentile
Class share: 10% train vs 6.4% test
Imbalance handled with class_weight="balanced"

## Slide 18: Classifier performance
Chart: 
| Accuracy | Precision | Recall | F1
Logistic Reg. | 0.84 | 0.287 | 1 | 0.446
Decision Tree | 0.936 | 0.5 | 0.663 | 0.57
Random Forest | 0.97 | 0.769 | 0.756 | 0.762
Random Forest: best F1 (0.762)
Logistic: perfect recall but 28.7% precision
Tree: middling on both

## Slide 19: Random Forest confusion matrix
2,469
True normal
39
False alarm
42
Missed flood
130
Caught flood
Predicted: normal | high
Precision 76.9%, recall 75.6%
Logistic Regression catches all 172 floods but raises roughly 430 false alarms (derived from its precision)
Flood warning favours recall; trust needs precision: tune the threshold

## Slide 20: What signals a high-flow day?
Chart: 
| dew point | rain sum 7d | discharge (today) | rain mean 7d | month | humidity | discharge lag 1 | rain sum 3d | discharge lag 2 | discharge mean 7d
Importance | 0.094 | 0.091 | 0.087 | 0.085 | 0.068 | 0.062 | 0.06 | 0.058 | 0.047 | 0.045
Importance is spread out, unlike regression
Accumulated 7-day rainfall and humidity matter for flood onset
Month encodes monsoon timing

## Slide 21
Conclusion
Next-day river-discharge prediction using weather, river history, seasonality and station information
72.46 m³/s
AUGUST MEAN DISCHARGE
15.04 m³/s
BEST RMSE · LINEAR REGRESSION
2.42 m³/s
LOWEST MAE · RANDOM FOREST
0.762
BEST CLASSIFIER F1 · RF
REGRESSION FINDINGS
HIGH-FLOW CLASSIFICATION
Discharge showed strong seasonality, peaking in August at 72.46 m³/s on average.
Linear Regression led on RMSE (15.0433) and R² (0.9344); Random Forest led on MAE (2.4167 m³/s).
Feature engineering reduced Random Forest MAE by 2.19% and RMSE by 6.54%.
High flow was defined as next-day discharge above each station’s training-set 90th percentile; positives were 10% of train and 6.4% of test.
Random Forest achieved 97.0% accuracy, 76.9% precision, 75.6% recall and the best F1 (0.762).
Logistic Regression reached 100% recall but only 28.7% precision, producing many false alarms.
NEXT STEP Tune the decision threshold to balance missed high-flow events against false alarms; validate with a persistence baseline and station-level metrics before operational use.
The 90th-percentile labels are statistical thresholds, not official warning levels. Results reflect one chronological test period.